## Slide 1: 3D Scene Reconstruction
General goal: 3D reconstruction using a hand-held ToF/Kinect
Challenges:
  Simultaneous estimation of camera pose & data fusion
  Real-time processing of a lot of data (>500 M pts/min)
  Range data is noisy and has potentially only few features for camera tracking
  Dynamic scene content
Typical setup
Noisy depth data
RGB data
3D reconstruction result
Notes: This slide should be self-contained

## Slide 2: Pipeline: Point-Based Reconstruction
  Find matching model points for given input point
  Iterative Closest Point (ICP)
  Model points and input points are merged together:
    Position, orientation, local curvature
  Point-based rendering
  Use high quality on-the-fly surface reconstruction
Current Model
Close-up
New input data
Index map (model data)
Notes: General approach:
Camera pose estimation using ICP assumes static scene
  Correspondance finding needs surface rendering
Classical approaches store density functions on volume grids
  Pro: Fusion in grid is easy, surface rendering is easy
  Con: Lots of data, fixed resolution
Storing only points is more storage efficient, but requires
  Efficient and high quality surface rendering (using curvature information makes better surfaces)
  correspondances between incoming and model points for fusion (idea: render model point indices instead of geometry allows for finding correspondances

## Slide 3: Precision & Memory Efficient
Notes: Main message:
Point based representation is efficient (1:100 compression)
Total amount of storage is less the same a one input frame

## Slide 4: Handling Dynamic Objects
Approach:
  Dynamic object is fully segmented
  Use divergence with respect to rigid camera motion

## Slide 5: Handling Low Feature Scene
Brick-Wall data set using the Kinect ToF
≤ 4 mm depth features
Ghosting due to
lost camera
tracking
Robust
camera
tracking